## Slide 1
AI-Powered Smart Bioreactor for Optimized Biofuel Production
Abdulhameed Alsaif, Ali Almatrood, Haidar Alnasser, Mohammed Albasarah Coach: Fadi Al-Badour
TEAM
010
Conventional bioreactors often suffer from inefficiency and high operational costs due to static operating conditions. Small variations in pH, temperature, and mixing can drastically reduce biofuel yield.
Background
Key Constraints
Prototype Development
Validation & Verification
Budget: Total cost must be < 6,000 SAR.
Safety: System must be vented and non-pressurized).
Modularity: the system must be modular.
Software: the system must use an open-source software.
Aspen Plus simulation verified the process thermodynamics, confirming an upgrade from ~6% wt ethanol in broth to 85% v/v in the final product stream
Problem Statement
Traditional lab-scale bioreactors rely on fixed recipes and manual adjustments. This leads to inconsistent yields and wasted energy because they cannot adapt to real-time fluctuations in pH or temperature.
Objective: To design, build, and validate a 10 L AI-driven bioreactor that uses closed-loop control to stabilize fermentation conditions.
Solution: An integrated system that automates temperature, pH, and mixing to increase ethanol yield and minimize power consumption
Specifications
Temperature Control: Maintain the setpoint within ±1 °C to ensure stable fermentation conditions.
pH Regulation: Keep pH within ±0.5 units of the target value for optimal microbial activity.
Agitation System: Provide variable speed mixing in the range of 100–500 RPM, allowing flexibility for different process needs.
Energy Efficiency: Ensure the average power draw remains below 500 W, supporting sustainable and cost‑effective operation.
Optimality: achieve >90% of the theoretical yield under optimal conditions
Control: Raspberry Pi 5 + ADS1115 architecture handling real-time data acquisition from industrial sensors.
Closed‑Loop Actuation: Control logic drives the DC motor and dosing pumps via real‑time sensor feedback, correcting deviations automatically
Optimality: the system has an optimal layout+ Silver meal heuristic for production management
AI: reinforcement learning model integrated with the dashboard to get an insights of the process.
Conclusion
Functionality: Built a working 10 L smart bioreactor integrating mechanical, electrical, and chemical subsystems.
Efficiency: Operates at ~50 Wh/L, well below the energy limit, enabling renewable integration.
Impact: Modular, open‑source design supports lab‑scale biofuel research and sustainability goals.