## Slide 1
AI-Driven LiDAR Navigation Glasses with Adaptive Haptic Guidance for the Visually Impaired
Fahad Khamis, Mohammed Almadani, Mohammed Aljamili, Ahmed Alajrafi Coach: Dr. Firas Alhindawi
TEAM
014
Visually impaired people rely mainly on canes and audio cues, which provide limited information about where obstacles are and at what distance. Our goal: augment, not replace, existing tools with a hands-free, quiet, haptic “sixth sense” for nearby obstacles.
Problem Statement
Validation & Verification
Conclusion
Power/mAP/Delay/Classification
Our project turns 3D vision into simple, directional neck vibrations, giving users an extra “sense” for nearby obstacles without sound, screens, or hands. Our prototype meets its key design targets for latency, battery life, privacy, RAM usage, and comfort, proving that a small, low-cost wearable can deliver meaningful spatial awareness in real time.
Specifications
detect 5 classes (car, person, chair, door, tree) with mAP of ≥ 83% overall.
3-level spatial haptics mapped to left / center / right neck motors.
Local processing and unnecessary ports closed
Modification ability stored in a <5 kB config file.
≤ 2 min time from power-on to ready.
Non-conformance rate <6% & 95% CL, with SPC p-chart (CL±3Ꝺ)
Constraints
RAM use: avg ≤ 70% of 8 GB.
Ergonomics: neckband fits ≥ 90% of adult head/neck sizes.
No personal video or location data stored & unnecessary ports closed.
Benefit-to-cost ratio ≤ 1.5.
Integrated Specifications
Battery life: ≥ 1-hour continuous use.
Weight: ≤ 650 g (belt + electronics + power bank).
Latency: end-to-end ≤ 1000ms latency.
Cost: total hardware cost < 5500 SAR.
Prototype Design
RAM Usage
Privacy & Local processing
Validation & Verification
Non-Conformance Rate
Weight