## Slide 1
IAM3D Remote Operations Vehicle for the Excavation of Resources (R.O.V.E.R)
Moath Alqahtani, Omar Modaihij, Mashae Alzabi, Abdulziz Algasham Coach: Dr. Muhammad Emzir
TEAM
021
This project was developed for the ASME IAM 3D Competition, where teams must design and 3D printed rover from scratch to excavate, transport, and deposit resources under FPV control within strict size, time, and safety constraints.
Situation
Prototype Design
Testing and Validation
Size (30.48 × 30.48 × 30.48)
Problem Statement
Objectives
Constraints
Specifications
Winning Strategy
Conclusion
Design and fabricate a mostly 3D-printed FPV-controlled rover that can reliably excavate, transport, and deposit resources within 5 minutes
Design a functional 3D-printed FPV rover
Apply optimization and safe system operation.
Excavate, transport, and deposit resources efficiently
4S Battery & Physical Kill switch
Springs Max D=1.27 cm, L=5.08cm
3 min setup & 5 min run limit
Chassis must be 3D printed
Operated via FPV
Transport and deposit at least 50 g of resources within the 5-minute
Excavation system must handle resource objects sized between 1 cm³ and 10.16 cm³.
FPV system high-quality continuous video
6. Vehicle weight not exceed 4.5 kg
Phase I: Exploration first (30s)
1
Detect metals
Scan Strategies
+
=
Domain
Knowledge
Phase 2: Optimization
2
Live Solution Dashboard
Full MIP Model (integrated)
For more information and videos, please visit the QR code
Simulated many scenarios through valid Models
Dual FPV cameras (front + arm)
3D-printed chassis engineered for strength, low weight
Multi-joint robotic arm with high-torque servos enables scooping, gripping
Raspberry Pi handles PS4 input
Two Arduino Unos split control
Integrated kill switch ensures instant system shutdown
TPU terrain-adaptive wheels with strong grip for sand
The project successfully developed a functional, 3D-printed, FPV-controlled rover with a robotic arm to reliably excavate, transport, and deposit resources within the 5-minute competition limit