## Slide 1
Smart Fire & Emergency Guidance System
Abdullah Aslan, Mahmoud Alhussen, Ayman Almutairi, Mahmoud Khatiri
Coach: Dr. Mansour Alharthi
TEAM
024
Fire incidents are among the most frequent causes of injury, loss of life, and property damage worldwide. Conventional smoke detectors, though widely available, provide only limited functionality.
The Smart AI-Powered Fire Guidance System address these shortcomings through an integrated network of intelligent sensor nodes capable of detecting multiple fire indicators smoke density, gas concentration, temperature and humidity and processing them using on-device algorithms. The system determines the probable fire location, evaluates whether local suppression is safe, and communicates evacuation or mitigation instructions to users through a connected mobile application.
Introduction
Prototype
The prototype have three sensors. An MQ-2 Hydrogen gas sensor that detects general smoke particles. A DHT11 temperature & humidity sensor module used to track ambient conditions and provide context that helps reduce false alarms. An MQ-135 Air Quality/Gas sensor which measures harmful gasses and checks for dust that could result in false alarms.
All sensors are linked to an ESP-32 microcontroller. That communicates via Wi-Fi or Bluetooth to the system’s cloud and mobile-app layers.