## Slide 1
Self-Balanced Pediatric Lower-Limb Exoskeleton
for Children’s Gait Rehabilitation
Khaled Mahmoud, Sameer Alsaba, AlMoayad Alsadi, Jehad Alsulami, Saad Alshami, Khalid Alsaeed Coach: Dr. Mohamed Faten Zhani
TEAM
007
Problem Statement
Design a child-specific lower-limb exoskeleton for supervised rehabilitation outside clinics.
Children with gait impairments need frequent rehabilitation.
Current therapy is manual and clinic dependent.
Most existing exoskeletons are designed for adults.
Goal: safe and lightweight gait assistance for children.
Introduction & Problem
Key Constraints & Specifications
Prototype Design
Results & Conclusions
Carbon fiber mechanical frame.
Hip and knee geared motors.
IMU, encoders, and foot sensors.
STM32 based control with safety features.
Operating Modes
Standing support.
Assisted walking.
Rehabilitation / training.
Emergency stop.
Manual height adjustment with locking pins.
Inline motor mounting to reduce bending moments.
Total mass ≤ 18 kg. Lightweight, high strength structure.
Operates at 0–40 °C.
Sized for pediatric users.
Structural safety factor > 2.
Stable control response achieved.
System is technically feasible for pediatric rehabilitation.
Future work: clinical testing and control refinement.
Conclusion
Final design is technically feasible, child-specific, and safety-focused.
Future work: hardware identification, clinical testing, adaptive control refinement.
4