## Slide 1
Sustainable Water Management: Filtration and Reuse of Wastewater from Car-Washing Stations
Advisor: Dr. Ismail Ibrahim Al Maraj
Yasser Alzahrani(ISE), Hamad Alduayj(CHE), Mohammed Alfarhan(ISE), Abdullah Alridy(CHE), Osamh Fnais(ME)
Car washes waste vast amounts of water, raising costs and harming the environment. Existing
systems are expensive, inefficient, and unsustainable, making water recycling a challenge for businesses aiming to cut expenses and reduce environmental impact.
User Training: The system should not require training for employees in maintenance and operation..
Energy Efficiency: The filtration system must incorporate solar panels to supply at least 35% of its energy needs.
Area: The target range for system size should not exceed 2*1.5 m2.
Oils: must remove the oil from the water before introducing water to the filtering material.
Water Temperature: should be between 20-45
oC to prevent paint damage.
pH: must be between 6.5 - 7.5 to ensure neutralized water.
Total Dissolved Solids (TDS): less than 150 ppm to avoid scaling and deposits.
Hardness level: should be between 75-150 mg/L to prevent both scaling and corrosion.
Flow rates: the flow rate is 6.67 L/m where we have 100 L and 15 minutes.
ORP between 200 to 300 mV to provide enough oxidizing potential to clean effectively.
Problem Statement
Testing/Validation
Prototype Design
We sincerely thank Dr. Zyad Lesman and Dr. Ismail Ibrahim Al Maraj for their invaluable guidance and support. Our gratitude also goes to KFUPM for providing financial support and resources for the prototype development. Lastly, we thank our design team for their hard work and dedication.
Acknowledgements
This project developed an optimized water filtration system for car wash wastewater, featuring a multi-stage process including oil catch, screen filter, sand filter, resin filter, and activated carbon. The system ensures water quality suitable for reuse, with a focus on efficiency, minimal maintenance, and sustainability for car wash operations.
Conclusion
Equations
Constraints
Specification
Pump Power:
𝑃 = ρ ∗ g ∗ Q ∗ H
ρ = Density of water (1000 kg/m3 ).
g = Gravitational constant (9.81 m/s2). Q = Flow rate (m3/s ).
H = Total head loss (m).
Solar panel power:
solar
P = Power required by the solar panel
(W).
1.25= Safety margin (dimensionless).
0.35= Fraction of the energy provided by the solar panel (dimensionless).
Ppump= Power consumed by the pump (W).
Tpump= Operating hours of the pump per day (h).
Tsun peak = Peak sun hours per day (h).
Quality Control Chart
Parameters before filtration
Parameters after filtration