## Slide 1
Optimization of Steam Distribution System Through Utilization of Lost Pressure
FAISAL ALMESNED
MOHAMMAD ALQAHTANI
SALMAN SHEBAM
HUSSAIN MASOUD
KUMEL MASHAL
Group: 78
Introduction
Background:
Sabic Utility uses 7 boilers to produce steam at various levels for use in chemical plant
Three levels of steam: HP,MP, and LP
Testing/ Validation
Conclusion
Graphs and Charts
Final Design Calculations
CHEMICAL ENGINEERING
CHEMICAL ENGINEERING
CIVIL ENGINEERING
MECHANICAL ENGINEERING
MECHANICAL ENGINEERING
Specifications |  | Large Turbine (HP to MP) | Small Turbine (MP to LP)
 | Metric | Value | Value
 | Steam condition (inlet) | 45 bar & 400°C | 20 bar & 220°C
 | Steam condition (outlet) | 20 bar & 220°C | 7 bar & 165°C
 | Steam flowrate (inlet) | 500 ton/h | 375 ton/h
 | Steam flowrate (outlet) | 500 ton/h | 375 ton/h
 | Length | 16 m | 10 m
 | Width | 6m | 4 m
 | Height | 6.5m | 5.5 m
 | power produced | 22.31 MW | 15.92 MW
Constraints | 1.Steam demand variability in the 2.Pressure and temperature drop across turbines | Pressure Level | HP | MP | LP
 |  | Total Demand | 961.9 | 609.3 | 685.5
 |  | Total steam used for all conditions | 2256.7 |  | 
 | Pressure drop across turbines |  |  |  | 
 |  | Average Demand | 400 | 250 | 750
 |  | Total steam used for all conditions (assuming no steam excess) | 1400 |  | 
Prototype Design
Problem statement:
The reliance of pressure reducing valves and DS wastes the thermal potential energy of high pressurized steam.
No alternative pathway for the steam incase of maintenance or shutdown.
Proposed solution:
Proposes a bypass system with a steam turbine to recover lost energy, improving efficiency.
Enhances mechanical power generation and provides operational flexibility.
The prototype is significantly smaller than the actual final design, a scale down is done to do the comparison
Power of large turbine if 100% efficiency = 30.02 MWh
Expected power from prototype (0.4)x(0.9) efficiency since it is lower than 100W =
Actual measured power of prototype =
Specification is met since <
The design is innovative and practical approach to sustainable energy recovery
Optimizes turbine output and steam efficiency.
Affordable solution balancing environmental sustainability and functionality.
Potential improvements:
Use of advanced materials for enhanced durability.
Integration of smart monitoring systems for real-time optimization.
Specific enthalpy at
Specific enthalpy at
Time = where m is the water content for this prototype, the time is between 45-90 minutes depending on the water amount
Time to reach specific conditions:
Foundation Column Dimensions | Symbol | Dim (cm)
 | C1 | 120 * 120
 | C2 | 110 * 110
 | C3 | 98 * 98
 | B1 | 100* 120
 | B2 | 50 * 120
 | B3 | 50* 120
Structural Parameters | Parameters | Value
 | ƒ'c (Mpa) | 70.00
 | ƒy (Mpa) | 420.00
 | qult (Kpa) | 257
 | Mu (KN) | 280
 | Maximum Settlement in 150 year (mm) | 23.7
HP – MP |  | Turbine Design (Large)
10000 | RPM | 
2 m | Diameter pitch | 
5 | Number of stages | 
38 | Number of blades in ring | 
2.4 m | Blade height of stage 1 | 
3.3 m | Blade height of stage 2 | 
4.5 m | Blade height of stage 3 | 
5.8 m | Blade height of stage 4 | 
7.3 m | Blade height of stage 5 | 
44 kJ/kg | Drop of enthalpy in stage | 
MP – LP |  | Turbine Design (Small)
8000 | RPM | 
2 m | Diameter pitch | 
4 | Number of stages | 
44 | Number of blades in ring | 
3.4 m | Blade height of stage 1 | 
5.4 m | Blade height of stage 2 | 
6 m | Blade height of stage 3 | 
7 m | Blade height of stage 4 | 
44 kJ/kg | Drop of enthalpy in stage | 
Nozzle Design (Small) | MP – LP | 
 | RPM | 8000
 | Diameter pitch | 2 m
 | Number of stages | 4
 | Number of blades in ring | 44
 | Blade height of stage 1 | 3.4 m
 | Blade height of stage 2 | 4.4 m
 | Blade height of stage 3 | 5 m
 | Blade height of stage 4 | 6.1 m
 | Blade height of stage 5 | 44 kJ/kg
 | Drop of enthalpy in stage | 8000
Nozzle Design (Large) | HP – MP | 
 | RPM | 10000
 | Diameter pitch | 2 m
 | Number of stages | 5
 | Number of blades in ring | 38
 | Blade height of stage 1 | 2.4 m
 | Blade height of stage 2 | 3.3 m
 | Blade height of stage 3 | 4.5 m
 | Blade height of stage 4 | 5.8 m
 | Blade height of stage 5 | 6.3 m
 | Drop of enthalpy in stage | 44 kJ/kg