## Slide 1
Electrodynamic Self-Cleaning System for Solar Panels
Aljouri Zebany, Asma Alatawi, Rawan Aldamkh, Fatima Al Saif, Sajedah Alghazwi, Rawan Asiri Coach: Dr. Junaid ur Rehman
TEAM
F34
Problem Statement
Prototype Design
Testing & Validation
Conclusion
An autonomous system for removing dust from solar panels using optimized electrodes, thresholds, a durable frame, and an LLM-powered dashboard, improving cleaning efficiency while reducing water use in arid environments.
Solar PV systems in dusty environments suffer from performance degradation due to dust accumulation. Existing solutions rely on manual or water-based methods that are labor-intensive, costly, and unsustainable in arid regions like Saudi Arabia.
Our Solution: EDS
The Electrodynamic Self-Cleaning System uses high-voltage, low-current AC signals on transparent electrodes to create an electric field that removes dust without water or manual cleaning, supported by a smart monitoring platform.
Before Cleaning
After Cleaning​
Power Supply
Electrode Sheet
Frame
Monitoring
Objectives
Efficient cleaning
Low energy consumption
Smart automation
Reliable monitoring
Sustainable design
Optimized threshold-based activation
Specifications
Power Supply | 3-phase, 120° ±5°, 50% duty cycle and ≤ 5 Hz
Control | Dual optimized thresholds
Transparency | ≥70%
Installation | ≤15 min/panel
Monitoring | ≤5 min delay
Weight | ≤5% of panel
Cloud Data | ≥85% transmission , 30-day storage
AI Insights | ≤5 min
Constraints
Voltage | 1 kV ±10% (Max 1.2 kV)
Environment | −20°C to +80°C
Budget | ≤15,000 SAR
Connectivity | ≥85% uptime
Power | ≤10% of output
Security | Backend-only API keys
Three-phase with 1.2 kV peak,120° phase shift and 50% duty cycle
Best cleaning achieved at 3 Hz with tilted spiral design
Measured transparency 70%, within acceptable light transmission
Optimal thresholds identified from real data, achieving ~85% efficiency under all constraints
Real time dashboard and LLM insight generation within 10 seconds
Frame weight validated at 2.75% of panel weight, well below the 5% specification limit
>75%
Cleaning Efficiency
≤20 W/m²
Power Consumption
min
Environmental detection