## Slide 1
Smart Glove for Translating Sign Language into Speech
ICS: Jude Alharbi, Shahad Sulais, Rahf Altwairqi, EE: Raghad Alqahtani, Sadeem Alshaly, ME: Lama Alzahrani Coach: Dr. Junaid ur Rehman
TEAM
F35
Hearing-impaired individuals face communication barriers due to limited interpreters. This project develops a smart glove enabling real-time, two-way communication by translating Arabic Sign Language to speech and speech to text.
Testing and Validation
Conclusion
Natiq Glove was successfully developed by integrating hardware and software to enable reliable, real-time, two-way communication. The system translates Arabic Sign Language into speech and speech to text, improving accessibility and supporting Saudi Vision 2030.
Information & Computer Science
Electrical Engineer
Prototype Design
Introduction
Collected and preprocessed data, trained an Extra Trees model, and enabled real-time prediction with smoothing.
The system successfully met specifications with reliable recognition of 11 gestures.
The components successfully met specifications with ≤ 6 MPa, FOS ≥ 1.5
The total system weight is 212.1 grams
The total prototype cost is 1650 ﷼.
Natiq uses camera-based translation when the glove isn’t available.
Mechanical Engineer
The system was validated by measuring 3.3 V and 130 mA using a multimeter, achieving a charging time of 1.5 hours and an operating time of 6 hours, with Bluetooth connectivity up to 5 meters.
ESP32: Processes data & controls communication
Flex Sensors: Detect finger movement
MPU6050: Detects handmotion (pitch & roll)
Microphone: Speech-to-text (two-way communication)
Speaker (DFPlayer): Outputs speech
Power: 3.7V battery + boost + TP4056
Hardware Components
Application
Software Components
AI Gesture Recognition: ≥ 10 gestures
Bluetooth Range: ≥ 5 m
Recharge Time: ≤ 2 h
Response Time: ≤ 5 s
Operating Time: ≥ 6 h (3.7 V Li-ion)
Weight: ≤ 1 kg, evenly distributed
Audio Level: 40–80 dB
Structural Strength: ≤ 6 MPa, FOS ≥ 1.5
Learning Efficiency: ≥ 80% in 25 min
Font Size & Colours: ≥ 14 pt, readable
Bluetooth Standard: Version 5.0
Standards: IEC 62368-1, ISO 9241-210 compliant
Specifications
Constraints
• Prototype Cost: ≤ 3000 SAR per unit
• Operating: 3.3 V ± 5%, ≤ 500 mA
• Fabric Stress: ≤ 1.5 MPa
• Memory Usage: ≤ 75% flash memory, ≤ 70% RAM of the program