## Slide 1
Drone-Based Structural Crack Detection and Classification Inspection System
Mohammed Aldahash, Faisal Alabduljabbar, Mohammed Almezail,
Abdulrahman Aloufi, Alwaleed Almutairi, Mohammed Alolayan Coach: Esam Alhomaidi
TEAM
M002
A semi-autonomous drone system tailored for low-rise buildings that detects, classifies, and assesses structural cracks. It combines drone inspection, onboard AI model, crack measurement, and automated reporting to insure fast and clear building assessment.
Introduction
Prototype
Testing & Validation
Constraints & Specifications
Validating a successful simulation mission with low-latency live video.
Problem Statement
Conclusion
Deliverables
Manual crack inspection is slow, expensive, and unsafe. Existing drones only capture images, but engineers still need to review defects. Our system closes this gap by turning inspection data into actionable crack information.
Prototype proved that drone-based crack inspection can be safer, faster, and more consistent than manual methods. It integrates detection, classification, measurement, and reporting in one workflow offering a solution to low-rise buildings.
The drone includes an S500 quadrotor, Pixhawk controller, Raspberry Pi 5, and Intel RealSense D435 camera.
The model performs structure scanning, revisits detected cracks, measures depth, and generates a final inspection report.
Validating an AI model trained on a 1,400+ image dataset, reaching 65% accuracy in crack detection.
Validating successful drone flight and stable hovering.