## Slide 1
Advanced HVAC System for Thermal Comfort & Energy Optimization in Offshore Rig Cabins
Abdullah Alqurashi, Nawaf Al Thawab, Saed Althalabi, Fahad Alaqeeli, Nawaf Aljohani, Abdulrahman Alhaidari
Coach: Ahmed Al-jabr
TEAM
M010
Offshore cabin HVAC systems consume a significant share of auxiliary power. Most still rely on fixed setpoints and fixed-direction diffusers, resulting in occupancy-insensitive cooling and inefficient air delivery. Condenser fouling further degrades heat transfer and increases energy use over time.
Background
Problem Statement
Objective
Prototype Design
Design, build, and validate an integrated HVAC prototype for an offshore-scale cabin that maintains 22–25 °C and 40–60% RH while reducing energy use through computer-vision occupancy sensing, a four-nozzle smart diffuser, an OR/SPC supervisory layer, and automated condenser self-cleaning.
Conventional offshore-cabin HVAC control is occupancy-blind, airflow-fixed, and fouling-exposed, producing avoidable energy waste, uneven comfort, and progressive efficiency loss.
The project delivered a five-discipline integrated HVAC prototype with smart airflow, automated condenser self-cleaning, and real-time supervisory control, successfully meeting all defined specifications and constraints. It achieved at least 85% occupancy detection accuracy, maintained stable comfort conditions, met the required EER, restored comfort within 5 minutes of state changes, and integrated a live dashboard with SPC monitoring alongside an OR supervisory decision layer.
Constrains
Specifications
Integrated Specifications
Testing & Validation
Conclusion