## Slide 1
AI-Driven Automated Gearbox Failure
Diagnostic Rig
Abdullah Alotaibi (ME)​, Abdullah Alammari (ME)​, Fahad Almutairi​ (CS), Mana Al Abas (CS), Khalid Al Saif (COE), Mohammed Aman​ (EE) Coach: Dr. Bilal Qureshi
TEAM
M049
This project builds a vibration-based diagnostic rig with AI to detect existing faults and prevent repeat failures.
Problem statement
Prototype Design
Testing & Validation
Conclusion
4
Motor & VFD
2.2 kW rated Gearbox
Brake Controlled via KTC-812
Mechanical Assembly
Block Diagram
Constraints
C1: The rig should only be able to work on single stage spur gearboxes
C2: speed shall be controlled by a PID controller
C3: The UI allows to input test parameters and displays visualizations
Specifications
S1: Gearbox handle power of 2.2 kW
S2: Accelerometer noise level < 50 mV
S3: Classification accuracy ≥ 75%
S4: Sampling ≥10 kS/s per channel
S5: Response time should be ≤ 2s.
Vibration sensor 1
Vibration sensor 2
VFD
Brake controller
ESP 32
Software & ML model
Healthy condition (S3)
Chipped condition (S3)
Missing condition (S3)
The project successfully managed to:
Provide diagnosis accuracy ≥ 75%
For future work, improving system to accommodate for diverse gear types.
2.22 kW from VFD (C2, S1)
Single stage spur gearbox (C1)
Accelerometer noise (S2)
sampling per second (S4)
Response time (S5)
UI (C3)
User Interface