## Slide 1
IAM3D Remote Operations Vehicle for the Excavation
of Resources (R.O.V.E.R.)
Abdullah Alashban, Suliman Alsobi, Yaser Alqahtani, Moataz Alqahtani, Ali Aldahwali, Ahmed Albalawi Coach: Eng. Mohamed Ahmed
TEAM
M086
FPV rovers exist for teleoperation, but none combine sand excavation, compact additive manufacturing, and a precise fast arm in one safety-compliant design.
Testing and Validation
Problem Statement
Project Objective
Constraints
Specifications
Build a compact FPV rover that moves fast on uneven sand terrain, transports heavy excavated material reliably, and operates a precise, safe robotic arm for resource collection and deposit.
Conclusion
Measured rover mass: 5.3Kg
Power Distribution Efficiency under stall load: 91%
Rover speed measured on sand surface: 0.66 m/s
Added 3 fuses for extra safety
1 | Size (30.48 × 30.48 × 30.48)
2 | Batteries max 4S configuration and must have a kill switch
3 | Chassis must be fabricated using additive manufacturing
4 | FPV control and camera system shall maintain signal range >20 m
5 | Power distribution efficiency >85%
Prototype Development
1 | 3D-printed parts ≥ 70% of total part count
2 | Transport ≥ 150 g of mixed resources with >0.1 m/s on sand
3 | Controlling the ROVER using a wireless controller with >20 m range
4 | All subsystems operate with no fault ≥ 3 consecutive runs
5 | The scoop shall collect ≥ 150g of mixed resources
FPV
(First Person View)
RC
Arduino Mega
FPV camera provides live visual feedback
TPU Material for more resistance on sand
Hight Torque Motores for heavy weight lifting
Full 3D additive material Designed and fabrication
Smart Ventilation Design for Electronics cooling
Differential locomotion type for easier manoeuvrability and Controllability
A compact, fully 3D-printed FPV
rover capable of precise sand excavation and resource deposit was successfully built and validated, meeting all speed, power, and arm performance targets.