## Slide 1
Reducing water cut in smart wells via ultrasonic sensors and flow control equipment
Mohammed Sahwan, Hadi Alsalem, Hassan Alshaer , Mohammed AlShareef, Abdulrahman Abdalla Coach: Dr. Ayman Al-Lehyani
TEAM
M106
Problem: Traditional water cut monitoring relies on surface measurements.
Solution: Installing an ultrasonic sensor in the downhole completion of the well to detect water encroachment
Introduction
Constraints
Prototype Design
Test & Validation
Pressure Safety: 1450 psi
Operating Temperature: 0 to 120°C
Hardware Efficiency: ≤ 16GB RAM
Fluid Density: ≥ 0.1 g/cm³ difference.
Power Consumption: Total ≤ 10W.
Processing Speed: latency ≤ 500 ms.
5
Specifications
Emulsion: Handles ≤ 90% emulsified volume.
Signal Quality: SNR ≥ 30 dB.
Electronics Power: Sensors < 3W.
Data Integrity: 99% logging success.
UI Latency: Dashboard updates < 1.0s.
Response Time: Valve trigger ≤ 2s. Model Logic: F1-Score ≥ 0.85.
Actuation: Valve closure ≤ 5s.
Measurement Cell (Pipes)
Ultrasonic Sensor
5 emulsion samples using crude oil with 28 API and synthetic formation water with a density of 1.13 g/cc
Arduino control unit (Mega 2560)
Conclusion
Velocity of sound in saline water = 1750 m/s
A constant volume of fluid was added, and measurements were taken from the sensors
Variation in the reading in oil sample is used (empirical correlation)
The prototype accomplished the main goal of phase detection. Although future improvements are required to optimize precision, this technology provides a highly practical solution for the oilfield.
Delayed Detection = Lost Production