## Slide 1: Autonomous Leveling Drone
`
Khalid Alshehri – Jafar Alhabeeb – Abdulmohsen Alsubaie – Mohammed Almutawa
Final Target Specifications:
Lifting Maximum Height: 10 m
Measurements Accuracy: 0.05 m
Flight Time: 7-13 min.
Target Area: 500 m^2
Project Statement: this project aims to develop a drone that utilizes elevation sensors to make leveling measurement controlled by a computer software.
Final Prototype
Design Process
Testing
Deliverables:
1. Prototype of the autonomous leveling drone. 2. Software to interface with the drone. 3. Altitude measurements of specified locations in (m) [area in front of building #3].
Constraints:
Stability of the drone while flying.
Smooth horizontal movements.
Limited fly time.
Limited budget
Conclusion and Points of Improve
Introduction
Function of Product
In this project we will be investigating the method of measurement using LiDar Distance Sensor along with GPS sensor.
Enter required path and checkpoints in software
Drone flies following the path
Send elevation data to software
Record measurement at each checkpoint
Using GPS, and LiDar Distance Sensor
Analyze data on software
Compare the findings
Equations needed to find the measurements from the drone:-
Prototype Details:-
Drone fly to the specified points (i.e., TP, TP2, and TBM1) and record readings of GPS & LiDAR sensor
GPS distance reading - LiDAR Distance Sensor = E(TP1)
GPS distance reading - LiDAR Distance Sensor = E(TP2)
GPS distance reading - LiDAR Distance Sensor = E(TBM1)
For example, To find the difference in elevation between any two points = E(TP2) - E(TP1)
Proof that specifications are met:-
time = capacity ×
discharge
𝐴𝐷𝐷
= 3.0 ∙ = 15ℎ = 9 𝑚𝑖𝑛
0.8
16
discharge
time = capacity ×
𝐴𝐷𝐷
Our original thrust goal was 2100g to achieve our goal of a weight double that of the drone. Now we know our drone is well above that goal at 2680g of thrust. For the drone to be lifted even slightly, the thrust needs to be equal to the weight of the drone. However, to have stable and higher height, the thrust needs to be double that of the drone. The thrust used is going to be enough thrust for the drone to fly over 10 m of height stably.
The flying time can be calculated using the following equations:
where capacity of our battery is 3000 mAh, discharge is 0.8 or 80%, and ADD can be calculated
as
𝐴𝐷𝐷 =
𝐴𝑈𝑊 ∙ 𝑃
𝑉
1.05 ∙ 170
=
11.1
= 16.08
which is in the range of specified of 7-15 min.
Our original thrust goal was 2100g to achieve our goal of a weight double that of the drone. Now we know our drone is well above that goal at 2680g of thrust. For the drone to be lifted even slightly, the thrust needs to be equal to the weight of the drone. However, to have stable and higher height, the thrust needs to be double that of the drone. The thrust used is going to be enough thrust for the drone to fly over 10 m of height stably.
time = capacity ×
discharge
𝐴𝐷𝐷
= 3.0 ∙ = 15ℎ = 9 𝑚𝑖𝑛
0.8
16
discharge
time = capacity ×
𝐴𝐷𝐷
The flying time can be calculated using the following equations:
where capacity of our battery is 3000 mAh, discharge is 0.8 or 80%, and ADD can be calculated
as
𝐴𝐷𝐷 =
𝐴𝑈𝑊 ∙ 𝑃
𝑉
1.05 ∙ 170
=
11.1
= 16.08
which is in the range of specified of 7-15 min.