## Slide 1
Design a sustainable & efficient residential building that supplies it energy need
Problem Statement
ZERO-Net Energy Building
Done by Fares Alqahtani, Abdulrahman Bukhari, Nasser Baarma, and Abdullah alhussain
Team 2 Instructor: Dr. Muhammad Emzir
Constraints
• Land Area 201.5 m2
• built-up area of 256m2 (villa with two-level)
• Overall Cost must not exceed 500,000 SR (estimated to be less than 440,00SR)
• Energy produced by the solar panels (250w/m2 )
• Average efficiency of PV panels is 20%
• Saudi Building Code (SBC):
➢ SBC 301 (Structural – Loading and Forces)
➢ SBC 602 (Energy Conservation – Residential)
➢ SBC 304 (Structural – Concrete Structures)
Technical Specifications
Off-grid System Capacity of 20kWh
Efficient Reinforcement Concrete Design (As min/ A req = 0.90)
Heat Insolation (U-value < 0.611 w/m^2k),(R-value > 1.5) m^2C/W
Efficient HVAC (5.0kWh)
A microcontroller with Bluetooth, 15 General-purpose input/output (GPIO) pins, and 10 analog input pins for every room
A user interface that is accessible through the internet
Grey Water System 2000-3000 L ( Total Tank Storage)
Concepts Evaluation
​ | Concept​ |  |  | 
Criteria​ | A​ | B​ | C​ | D​
Capital Cost​ | +​ | -​ | -​ | -​
Operation Cost​ | -​ | +​ | 0​ | -​
Reliability​ | -​ | +​ | +​ | -​
Sustainability​ | 0​ | 0​ | +​ | 0​
Production Carbon Footprint​ | +​ | -​ | -​ | -​
Operation Carbon Footprint​ | -​ | +​ | 0​ | +​
Client acceptance​ | +​ | 0​ | +​ | -​
Sum +’s​ | 3​ | 3​ | 3​ | 1​
Sum 0’s​ | 1​ | 2​ | 0​ | 1​
Sum -’s​ | 3​ | 2​ | 3​ | 5​
Net Score​ | 0​ | 1​ | 1​ | -4​
Rank​ | 3​ | 1​ | 2​ | 5​
Continue​ | no​ | yes​ | no​ | no​
Solar On-grid system
Solar Off-grid system with batteries
Solar Hybrid system
Solar Off-grid system with wind turbine
Analysis (Testing / Validation)
Months | Efficiency | PV Area ( m2) | Irradiation (kWh/m/D) | Number of panels | Avg Daily supply (kW) | Avg Daily Loads (kW)
January | 0.209 | 3.1 | 3.57 | 32 | 74.016096 | 48.78
Feb | 0.209 | 3.1 | 4.42 | 32 | 91.638976 | 55.68
March | 0.209 | 3.1 | 5.13 | 32 | 106.359264 | 87.5
April | 0.209 | 3.1 | 6.03 | 32 | 125.018784 | 89.61
May | 0.209 | 3.1 | 7.03 | 32 | 145.751584 | 92.5
June | 0.209 | 3.1 | 7.73 | 32 | 160.264544 | 95.67
July | 0.209 | 3.1 | 7.26 | 32 | 150.520128 | 99.28
August | 0.209 | 3.1 | 6.97 | 32 | 144.507616 | 102.51
September | 0.209 | 3.1 | 6.45 | 32 | 133.72656 | 95.22
October | 0.209 | 3.1 | 5.33 | 32 | 110.505824 | 90.69
November | 0.209 | 3.1 | 4 | 32 | 82.9312 | 75.22
December | 0.209 | 3.1 | 3.28 | 32 | 68.003584 | 47.22
GUI
User Interface
The cost of producing electricity from solar panels compared to the cost of producing it in other ways by using RED-SCREEN software.
Reducing the greenhouse gases by using redscreen
Prove how to save money by using red-screen softwere
Important Equation
Learned
Conclusion
The project contributes to solving global warming by reducing CO2 emissions from residential buildings at a reasonable cost. Additionally, it will be efficient for heat insolation and HVAC system which is proven by analysis.
Applied what we learn in courses before for example, the calculation of the U-value to get the suitable insolation material and the calculation of the power load for the equipment’s house.
Improvement